How do sub-grid uncertainties propagate into reservoir-scale flow predictions for carbonate reservoirs?

S. Geiger1, A. Al-Dhahli1, M.I.J. van Dijke1, M. Dentz2, and I. Neuweiler3

1Heriot-Watt University, Edinburgh, United Kingdom

2IDEA-CSIC, Barcelona, Spain

3University of Hannover, Hannover, Germany

ABSTRACT:  Continuum approaches in reservoir simulations assume that flow and transport processes below the scale of a grid block cell can be described by their aggregate averaged behavior. While this approach is very successful in clastic reservoirs, (fractured) carbonate reservoirs face additional challenges because of their multi-scale geological heterogeneity and complicated wettability distribution. Both types of heterogeneity lead to a broad spectrum of transition times, incomplete mixing of chemical components, and irregular saturation distributions. This should be adequately resolved across all length scales, including scales smaller than the size of a reservoir simulation grid block cell, to improve reservoir-scale flow predictions. This talk will present two examples to illustrate how sub-grid uncertainties impact reservoir-scale flow predictions. First, we will study how wettability distribution and displacement processes at the pore-scale affect oil production during tertiary gas injection on the reservoir-scale. Then we will demonstrate how uncertainty in the distribution of matrix block sizes and shapes within a single grid block cell impacts oil recovery in a fractured carbonate reservoir.