Pressure problem for multiphase filtration and parallel solution algorithms

P. N. Vabishchevich1, and  M. V.  Vasilyeva2

1Nuclear Safety Institute, Moscow, Russia

2Notrh-Eastern Federal University, Yakutsk, Republic of Sakha, Russia

ABSTRACT:  Mathematical modeling of multicomponent flows in porous media is great importance in oil and gas recovery. The basic model includes the continuity equations, the Darcy laws for each phase and algebraic expression for the sum of saturations. Primary computational algorithms are implemented for such problems using the pressure equation. In this paper, we highlight the basic properties of the pressure problem and discuss the necessity of their fulfillment at the discrete level. The resulting elliptic problem for the pressure equation is characterized by a non-selfadjoint operator. Possibilities of approximate solving the elliptic problem are considered using the iterative methods. Special attention is given to the numerical algorithms for calculating the pressure on parallel computers.