## Slide 1: Last Time
Magnetic Field of a Straight Wire
Magnetic Field of a Current Loop
Magnetic Dipole Moment
Bar Magnet

## Slide 2: Quantum Magnetism
Electron acts like spinning charge
- contributes to 
Electron spin contribution to  is of the same order as one due to orbital momentum
proton in nucleus also have spin but their ‘s are much smaller than for electron
angular momentum:
NMR, MRI – use nuclear 
Magnetic Moment = Orbital Motion + "Spin"
SPIN:
iClicker question:
Can Neutron has spin dipole moment?
A). No because neutron has no charge
B). Yes, because neutron is not the fundamental building block.
Notes: Neutron magnetic dipole moment is the same as proton and is not zero indicating smaller building blocks, i.e. quarks. For point particles, QM says gs = 2, which describe electron well. For proton gs ~5.6 and for neutron gs ~-3.8

## Slide 3: More for Today
Equilibrium vs. Steady State in a Circuit
What is "used up" in a circuit?
Kirchhoff's Current Node Law
E-field inside a wire

## Slide 4
iClicker Question
Why High Voltage is needed to transfer electricity?
Prevent animal from biting the cable.
Reduce energy wasted during transportation.
No reason. People started this way long time ago.
Notes: Asking student these questions to draw attentation.

## Slide 5
iClicker Question
Which way is preferred.
Left
Right
left and right are equal.
Notes: Asking student these questions to draw attentation.

## Slide 6
iClicker Question
Which of the following bulb will light up?

## Slide 7: Which of the two circuits shown will cause the light bulb to light?
Arrangement (a)
Arrangement (b)
Both
Neither
iClicker Question

## Slide 8
Water flowing in a pipe is similar to electric current flowing in a circuit.
  The battery is like the pump.
  The electric charge is like the water.
  The connecting wires are like the thick pipe.
  The filament is like the nozzle or narrow pipe.
  The switch is like the valve.
Notes: faucet

## Slide 9: We want to find out:
Are charges used up in a circuit?
Exactly how does a current-carrying wire create and maintain nonzero E inside?
What does the battery do?
Microscopic Questions:

## Slide 10: Conventional Current and Electron Current
C
Conventional
Current
+
+
+
Electrons exit battery at (-) terminal,
and enter battery at (+) terminal
Electron Current:
Positive charges exit battery at (+) terminal,
and enter battery at (-) terminal
Conventional Current:
C
Electron
Current
-
-
-

## Slide 11: Equilibrium vs. Steady State
http://physick.wikispaces.com/Electric+Current
Magnetic Field B
Current I
No current flows. Average drift velocity of electrons is zero
Equilibrium:
Current flows. Average drift velocity of electrons is constant
Current Flow is not Equilibrium, but it is Steady State.
Remember: Electrons flow in opposite direction
from conventional current I

## Slide 12: What IS the bulb using up?
1
2
C
Electron
Current
-
-
-
Can the bulb consume current by
destroying electrons?
 No.
Electrons cannot be destroyed.
Can the bulb consume current as
electrons accumulate in the bulb?
 No.
Otherwise electric field would change

## Slide 13: What IS the bulb using up?
1
2
C
Electron
Current
-
-
-
Chemical Energy of battery converts to:
Light Energy
Heat Energy

## Slide 14: Current Node Rule
A.K.A. Kirchhoff's Current Law
Current Node Rule: Current In = Current Out
Node: Any wire junction in the circuit.
Iin = 4A
Iout = 4A
Iin = 4A
I1-out = 1A
I2-out = 2A
I3-out = 1A

## Slide 15: Electric Field in the Circuit
Electrons can surf through a lattice
by finding the right wavelength.
But they do bump into lattice defects/deformations:
Need an Electric Field throughout the wire
to re-accelerate the electrons.
Collision!
Electron loses all
of its kinetic energy.

## Slide 16: Electric Field Inside the Wire
Constant current in the wire  Constant E in the wire.
I
I
I
I
I
I
I
I
Conventional Current
Drift Velocity controlled by |E|
Mobility (u) set by the material.
Constant current
requires constant |E|

## Slide 17: Direction of Electric Field in a Wire
Does current fill the wire?
Is E uniform across the wire?
E must be parallel to the wire
E is the same along the wire
0
0
VAB
VCD
Notes: B field measurements are the same all along the wire (unless we encounter loops).

## Slide 18: Electric Field in a Wire
E
Bulb filament and wires are metals –
there cannot be excess charges in the interior
Are excess charges on the battery?
ASSUME: E due to dipole field of battery.
E
E
What charges make the electric field in the wires?
This cannot be the source of the E which drives current.
Notes: SHOW THE BULB DEMO
There must be an electric field in the wires that is responsible for moving the charge carriers around the circuit.
The magnitude of E must be the same throughout a wire of uniform cross section and material.
The wire itself is electrically neutral, so there must be excess charges that give rise to the E-field.
If the excess charges were on the poles of the battery, we might expect the field to be greater closer to the battery. Moving the bulb closer to the battery does not change the current (as indicated by the brightness of the bulb). Also, changing the orientation of the bulb has no effect. If the excess charges responsible for the current resided on the battery poles, we would expect a directionality effect.

## Slide 19: Field due to the Battery
Surface charge arranges itself in such a way as to produce a pattern of electric field that follows the direction of the wire and has such a magnitude that current is the same along the wire.
E
Notes: If this were not the case, ie, if E varied along the length of the wire (of uniform area, material), we could not conserve charge. If the surface charge were distributed uniformly on the wire surface, current would not flow (no particular direction). Thus, it must not be distributed uniformly!

## Slide 20: Field due to Battery
Smooth transition from + surface charge to – to provide
constant E.
E
The amount of surface charge is proportional to the voltage.
Notes: Greater density of surface charge on right end of cylinder (representing the wire) than at left end. Hence, field along axis points to the right.

## Slide 21: Connecting a Circuit
What happens just before and just after
a circuit is connected?
Before the circuit is connected:
No current flows
System is in equilibrium:
+
+
+
+
-
-
-
-
How is |E| = 0 maintained when there are charges here?
There must be surface charges on the wire
to prevent current from flowing before we connect the circuit.

## Slide 22: Connecting a Circuit
Before the circuit is connected:
No current flows
System is in equilibrium:
Think about
the gap...
E due only to
gap faces
What happens just before and just after
a circuit is connected?

## Slide 23: Connecting a Circuit
Before the circuit is connected:
No current flows
System is in equilibrium:
Think about
the gap...
E due to
everything else
cancels Egap
What happens just before and just after
a circuit is connected?

## Slide 24: Connecting a Circuit
Now close the gap ...
E due to
everything else
cancels Egap
What happens just before and just after
a circuit is connected?
Before the circuit is connected:
The gap face charge  0, and so does Egap
No more
charges here

## Slide 25: iClicker Question
How would you expect the amount of
current at location 1 to compare to the
electron current at location 2?
A) There is no current at 2, since the bulb used it up.
B) There is less current at 2 than at 1, since some of it gets
converted to light and heat given off by the bulb.
C) The current at 2 is the same as the current at 1.
1
2
C
Electron
Current
-
-
-

## Slide 26: Connecting a Circuit
What happens just before and just after
a circuit is connected?
Just after the circuit is connected:
There is a disturbance in the
previous (equilibrium) E-field.
Now the region next to the disturbance
updates its E-field, and the next region...
How fast does this disturbance propagate?
At the drift speed of the electrons?
At the speed of light?
Notes: B
At the speed of the fields, which is at the speed of light.

## Slide 27: iClicker – Reality Physics!
Drift speed of electrons
Speed of light
Flip Light Switch On.
How long until electrons
from the switch reach the light bulb?
L = 5 m
A) About 1 nanosecond
B) About 1 microsecond
C) About 1 minute
D) About 1 day
Notes: D.
10^5 sec ~ 28 hours.
Images:
http://www.treeliving.com/home-lighting-–-how-save-energy
http://www.nrel.gov/news/features/feature_detail.cfm/feature_id=1616

## Slide 28: iClicker – Reality Physics!
Drift speed of electrons
Speed of light
Flip Light Switch On.
How long until information about the
change in E-field reaches the light bulb?
L = 5 m
A) About 16 nanoseconds
B) About 16 microseconds
C) About 16 minutes
D) About 16 days
Notes: A.
(5/3) x 10^(-8) sec ~ 16 x 10^(-9) seconds.

## Slide 29: Reality Physics!
Drift speed of electrons
Speed of light
Flip Light Switch On.
How long until information about the
change in E-field reaches the light bulb?
L = 5 m
≈ 1 day for electrons to travel from light switch to bulb.
≈ 16 nanoseconds for the change in E-field to travel from light switch to bulb.
Because there are sooooo many electrons
in the wire, they don't have to move far to
create a large current.
Notes: A.
(5/3) x 10^(-8) sec ~ 16 x 10^(-9) seconds.

## Slide 30: Connecting a Circuit
What happens just before and just after
a circuit is connected?
Just after the circuit is connected:
There is a disturbance in the
previous (equilibrium) E-field.
Now the region next to the disturbance
updates its E-field, and the next region...
The disturbance travels at the speed of light,
and within a few nanoseconds,
steady state is established.
Notes: B
At the speed of the fields, which is at the speed of light.

## Slide 31: Surface Charge and Resistors
After steady state is reached:
Notes: Just after connecting the circuit but before equilibrium is established, the electric field in the narrow resistor might temporarily be about the same as the electric field in the thick wires, leading to a comparable drift velocity. But since Athin is less than Athick, electrons accumulate at the right end of the thin wire, increasing the E field in the thin wire. Similarly, a deficiency of electrons develops at the left end because the number of electrons emerging from the wire is too small. These fields reach equilibrium when as many electrons leave the thin wire as enter. This happens when Ethin = Athick/Athin * Ethick.

## Slide 32: Energy in a Circuit
Energy conservation (the Kirchhoff loop rule [2nd law]):
V1 + V2 + V3 + … = 0 along any closed path in a circuit
Vwire = EL
Vbattery = ?
V= U/q  energy per unit charge
Notes: From charge conservation and definition of steady state: Node rule – tells us about relations between currents in different parts. But what about actual current? How large is it.
To answer – turn to energy conservation principle. Consider one electron as it is transported around the circuit.
Energy gained by e as it is transported between terminals in a battery is dissipated in the rest of the circuit.
Use round-trip.

## Slide 33: General Use of the Loop Rule
V1 + V2 + V3 + V4 = 0
(VB-VA)+ (VC-VB)+ (VF-VC)+ (VA-VF)=0
Notes: Add pics of coffeemakers, refrigerators etc. as elements in a circuit.

## Slide 34: Kirchhoff’s Rules
Kirchhoff’s Rule 2: Loop Rule
When any closed loop is traversed completely in a circuit, the algebraic sum of the changes in potential is equal to zero.
Kirchhoff’s Rule 1: Junction Rule
The sum of currents entering any junction in a circuit is equal to the sum of currents leaving that junction.
Conservation of charge
In and Out branches
Assign Ii to each branch
Coulomb force is conservative

## Slide 35: Circuit Analysis Tips
Simplify using equivalent resistors
Label currents with arbitary directions
  If the calculated current is negative, the real direction is opposite to the one defined by you.
Apply Junction Rule to all the labeled currents.
  Useful when having multiple loops in a circuit.
Choose independent loops and define loop direction
  Imagine your following the loop and it’s direction to walk around the circuit.
Use Loop Rule for each single loop
  If current I direction across a resistor R is the same as the loop direction, potential drop across R is ∆V = −I×R, otherwise, ∆V = I×R
  For a device, e.g. battery or capacitor, rely on the direction of the electric field in the device and the loop direction to determine the Potential drop across the device
Solve simultaneous linear equations
Notes: Current dirction is the moving direction of positive charge, i.e. the electric field direction, therefore, following the current direction, potential drops

## Slide 36: Loop Example with Two EMF Devices
Þ
If 1 <2, we have I<0 !?
This just means the actual current flows reverse to the assumed direction. No problem!

## Slide 37: Finding Potential and Power in a Circuit
Just means 0 V here
But what is I? Must solve for I first!
supplied by 12V battery
dissipated by resistors
The rest?
into 4V battery (charging)
Notes: Current dirction is the moving direction of positive charge, i.e. the electric field direction, therefore, following the current direction, potential drops

## Slide 38: Charging a Battery
Positive terminal to positive terminal
Charging EMF > EMF of charged device
Say, R+r1+r2=0.05 (R is for jumper cables). Then,
power into battery 2
battery being charged (11V)
good battery (12V)
If connected backward,
Large amount of gas produced
Huge power dissipation in wires

## Slide 39: Using Kirchhoff’s Laws in Multiple Loop Circuits
Identify nodes and use Junction Rule:
Identify independent loops and use Loop Rule:
Only two are independent.

## Slide 40: iClicker Question
What’s the current I1 ?
I1+I2
I2
I1
(a). 2.0A
(b). 1.0A
(c). -2.0A
(d). -1.0A
(e). Need more information to calculate the value.

## Slide 41
Replace by equivalent R=2 first.
Sketch the diagram
Simplify using equivalent resistors
Label currents with directions
Use Junction Rule in labeling
Choose independent loops
Use Loop Rule
Solve simultaneous linear equations
I1+I2
I2
I1

## Slide 42: Two Batteries in Series
Why light bulb is brighter with two batteries?
Work per second:
Two batteries in series can drive more current:
Potential difference across two batteries in series is 2emf  doubles electric field everywhere in the circuit  doubles drift speed  doubles current.
Notes: After getting i for both – ask how much brighter? How much more heat dissipate with 2 batteries?
In reality: not 4x because mobility changes with temperature., I.e. current also does not go twice up.

## Slide 43: Potential Difference Across the Battery
non-Coulomb force on each e
1. a=FNC/m
EC
FC
2. FC =eEC
Coulomb force on each e
3. FC =FNC
The function of a battery is to produce and maintain a charge separation.
Energy input per unit charge
emf – electromotive force
The emf is measured in Volts, but it is not a potential difference!
The emf is the energy input per unit charge.
chemical, nuclear, gravitational…

## Slide 44: Twice the Length
Nichrome wire (resistive)
Quantitative measurement of current with a compass
Current is halved when increasing the length of the wire by a
factor of 2.
Notes: Electric field is half -> half the drift speed -> half the current. Note that we are considering the wire to be a “resistive” wire.

## Slide 45: Doubling the Cross-Sectional Area
Nichrome wire
If A doubles, the current doubles.
Notes: Electric field in the wire doesn’t change when we use a thicker wire -> current doubles

## Slide 46: Two Batteries in Series
Why light bulb is brighter with two batteries?
Work per second:
Two batteries in series can drive more current:
Potential difference across two batteries in series is 2emf  doubles electric field everywhere in the circuit  doubles drift speed  doubles current.
Notes: After getting i for both – ask how much brighter? How much more heat dissipate with 2 batteries?
In reality: not 4x because mobility changes with temperature., I.e. current also does not go twice up.

## Slide 47: How Do the Currents Know How to Divide?
Notes: After connection there is a larger current through the battery and a larger gradient of surface charge along the wires to drive this larger current.

## Slide 48: Today
Transient response when connecting a circuit
How long until steady state is reached?
Introduction to Resistors
Energy conservation in a circuit
Kirchhoff's Voltage Loop Law
Batteries