## Slide 1: Please Fill the online Course evaluation.
http://www.purdue.edu/eval/
We now have 73 responses
Survey close on 04/30
This is the official survey requested by university

## Slide 2: Final Exam
* Friday: 05/05 in 7:00pm - 9:00pm in WTHR 200
* Chapters: all chapters but focus on 19, 20, 21, 22, 23 (4th edition)
* Makeup exam.
.approve only for valid reasons.
. If you need a makeup, please send me a request together with supporting
documents by 04/24 (Monday).
. Any requests after that will not be approved.
* Special needs
. If you has not contact me before, please bring me the letter from the Office
of the Dean of Students by 04/24 (Monday).
. Any request after that will not be approved.
* AOB
. multiple choice.
. Prepare your own scratch paper, pens, pencils, erasers, etc.
. Use only pencil for the answer sheet
. Bring your own calculators: graphic or scientific
. No cell phones, no text messaging which is considered cheating.
. No crib sheet of any kind is allowed. Equation sheet will be provided.
. 20 problems in total.

## Slide 3: Magnitude of the Transverse Electric Field
We got the direction.
Magnitude can be derived from Gauss’s law*
Field ~ -qa
1. The direction of the transverse
field is opposite to qa
2. The electric field falls off at a rate 1/r
* This was first shown by Edward Purcell, BSEE Purdue, Nobeal Laureate!
Notes: Derivation is too complex for this course
Kink in the electric field
Much slower than 1/r2 – makes it possible to affect matter that is very far from the accelerated charges – that is why we see very distant stars.
Quali

## Slide 4: Energy Flux: The Poynting Vector
The direction of the E/M radiation was given by
Energy flux, the “Poynting vector”:
S is the rate of energy flux in E/M radiation
It points in the direction of the E/M radiation
John Henry
Poynting
(1852-1914)
Note energy flux = [Energy/(time * Area)]
Energy flux = Intensity = [Power/Area] Same Thing!

## Slide 5: Momentum Flux
Net momentum:
in transverse direction: 0
in longitudinal direction: >0
Relativistic energy:
Quantum view: light consists of photons with zero mass:
Classical (Maxwell): it is also valid, i.e. momentum = energy/speed
Momentum flux:
Units of Pressure
Notes: N/m2 – units of pressure
S =[J/s/m^2}, so S/c = [N*m/(m^3)]=N/m^2

## Slide 6: Electromagnetic Spectrum
Notes: Microwave: not because it is used in microwave, but because it has ~micron wavelength
Visible – the whole spectrum from blue to red – the frequency barely changes twice!

## Slide 7: Radiation and Neutral Atom: Resonance
Amplitude of oscillation will depend on how close we are to the natural free-oscillation frequency of the ball-spring system
Resonance
This is why you can tune a radio
Notes: Organic molecules – electronic system is in resonance with E/M frequencies corresponding to ‘visible’ light

## Slide 8: Importance of Resonance
E/M radiation waves with frequency ~106 Hz has big effect on mobile electrons in the metal of radio antenna:
can tune radio to a single frequency
E/M radiation with frequency ~ 1015 Hz has big effect on organic molecules:
retina in your eye responds to visible light but not radio waves
Very high frequency (X-rays) has little effect on atoms and can pass through matter (your body):
X-ray imaging
Notes: Organic molecules – electronic system is in resonance with E/M frequencies corresponding to ‘visible’ light

## Slide 9: Color Vision
Three types of receptors (cones) in retina which incorporate three different organic molecules which are in resonance with red, green and blue light frequencies (RGB-vision):
Response spectra for three types of receptors
Max response wavelengths:
S – 440 nm (6.81.1014 Hz)
M – 540 nm (5.56.1014 Hz)
L – 560 nm (5.36.1014 Hz)
Refers to length of cone
Notes: Microwave: not because it is used in microwave, but because it has ~micron wavelength
Visible – the whole spectrum from blue to red – the frequency barely changes twice!
Three types of rhodopsin receptors contain three different opsin molecules (red, green, blue)
Cone absorption spectra: peaks at 440, 540, 560 nm (Short, Medium and Long – type cones, three types of opsin in rhodopsin)
http://psychlops.psy.uconn.edu/swadlow/Senpart2.htm

## Slide 10: Polarization of Electromagnetic Waves
Polarization is a measure of the degree to which the electric field (or the magnetic field) of an electromagnetic wave oscillates preferentially along a particular direction.
linearly polarized
unpolarized
partially polarized
Looking at E head-on
Linear combination of many linearly polarized rays of random orientations
components
equal y- and z-amplitudes
unequal y- and z-amplitudes

## Slide 11: Polarizer: polarization by absorption
An electric field component parallel to the transmission axis is passed by a polarizer; a component perpendicular to it is absorbed.
So if linearly polarized beam with E is incident on a polarizer as shown,
Zero if =/2, I0 if =0
If unpolarized beam is incident instead,
The intensity will reduce by a factor of two.
The light will become polarized along the transmission axis
transmission axis
dichroism (tourmaline, polaroid,…)

## Slide 12: iClicker Questions
A beam of un-polarized lights with intensity I is sent through two polarizers with transmission axis perpendicular to each other. What’s the outgoing light intensity?
½ I
2 I
0
1.5 I

## Slide 13: Example: two polarizers
This set of two linear polarizers produces LP (linearly polarized) light. What is the final intensity?
  P1 transmits 1/2 of the unpolarized light:
  I1 = 1/2 I0
  P2 projects out the E-field component parallel to x’ axis:
= 0 if  = /2
(i.e., crossed)

## Slide 14: Polarized Light
Polaroid sunglasses and camera filters:
reflected light is highly polarized: can block it
Considered: using polarized car lights and polarizers-windshields
Notes: Show trick with three polarizers – two crossed ones, add one at 45 degrees in the middle
Sheet of special plastic whose long molecules are aligned with each other
Sunglasses

## Slide 15: iClicker Questions
A beam of un-polarized lights with intensity I is sent through two polarizers with transmission axis perpendicular to each other. Then insert a third polarizer with ϴ What’s the outgoing light intensity?
Zero
Not zero

## Slide 16
7B-22 Polarizer Effects

## Slide 17: Polarized E/M Radiation
AC voltage
(~300 MHz)
What will happen if distance is increased twice?
no
light
E/M radiation can be polarized along one axis…
…and it can be unpolarized:
Notes: At every single time E is of course in just one direction, but it changes randomly and rapidly over time
Light from the sun is not polarized!

## Slide 18: UHF Transmitter and Dipole Receiver (6D-17)
Notes: Directions for doing the demo: Before powering the transmitter select the operating mode with the mode switch (preferably CW – continuous wave). Turn on the power to the transmitter. Move the receiver dipole close to the transmitter. The intensity of the lamp indicates the field strength of the signal. Move the receiver farther away and the light intensity diminishes. Rotate the receiver 90 degrees and the light goes out completely. Connect the receiver antenna to a voltmeter and you will get numerical readings indicating field strength of the signal.

## Slide 19
In which of these situations will the bulb light?
A
B
C
None
B and C
iClicker question
Notes: A

## Slide 20: Speed of light in medium
When light encounters an interface between different media, it can generally both reflect and refract.
Light can travel through matter medium as well as free space (vacuum). Inside matter, the speed of light v is generally less than c.
index of refraction

## Slide 22: Total Internal Reflection
In general, if sin 1 > (n2 / n1), we have NO refracted ray;
we have TOTAL INTERNAL REFLECTION.
All light can be reflected, none refracting, when light travels from a medium of higher to lower indices of refraction.
e.g., glass (n=1.5) to air (n=1.0)
But  cannot be greater than 90 !
Critical angle above which this occurs.
medium 2
medium 1

## Slide 23: Examples
Prism used as reflectors
(e.g., glass with n=1.5)
Notes: Field of vision

## Slide 24: Chromatic Dispersion
The index of refraction of a medium is usually a function of the wavelength of the light. It is larger at shorter wavelengths.
Consequently, a light beam consisting of rays of different wavelength (e.g., sun light) will be
refracted at different angles at the interface of
two different media. This spreading of light is
called chromatic dispersion.
White light: It consists of components of nearly all the colors in the visible spectrum with approximately uniform intensities.
The component of a beam of white light with shorter wavelength tends to be bent more.
Spectrometer (such as a prism)

## Slide 25: 7A-22 Refraction by Prisms
Glass
red
blue
Notes: A large Plexiglas prism is mounted on the lens board. A narrow beam of light is directed toward one side of the prism causing the light to be refracted. In addition to ordinary refraction, dispersion and minimum angle of deviation can also be shown.

## Slide 26: Why is the sunset red?
The shorter wavelengths of blue light are scattered by gas molecules in the atmosphere more than longer wavelengths such as red light.
When the sun is low on the horizon, the light must pass through more atmosphere than when the sun is directly above.
By the time the sun’s light reaches our eyes, the shorter wavelengths such as blue and yellow have been removed by scattering, leaving only orange and red light coming straight from the sun.
Why the Sky is Blue

## Slide 27: iClicker question: What’s the color of sky on the moon?
Blue
White
Red
Yellow
Black
Shadow indicate daylight time

## Slide 28: Mirage and Rainbow
water droplet
rainbow
red is outside.
intensity max at 42
Notes: Ripples, you can never catch the rainbow.